## Slide 1: cLHS using ArcGIS and R
An example from the Republic of Haiti

## Slide 2: cLHS using ArcGIS and R
The project area is ~7,800 acres, largely in the Plaine du Cul-de-Sac region of Haiti
The objective is to select representative sample points in support of a soil mapping project
Develop datasets of 150 and 300 samples to support availability of small or large field staff

## Slide 3: cLHS using ArcGIS and R
The following data layers were selected as strata:
  Slope gradient
  Slope curvature
  Wetness Index (aka topographic wetness index, compound topographic index)
5m resolution data, derived from 1m LiDAR used to develop layers

## Slide 4: cLHS using ArcGIS and R
5m resolution yields a population of 1.26 million points to draw from, or 162 points per acre
A machine with 8GB of RAM was unable to process this large dataset
It was considered overkill to draw from such a large population

## Slide 5: cLHS using ArcGIS and R
Reduce the population to an acceptable number
A 35m spacing was determined adequate, yielding ~26,000 points, or ~3 points per acre
Why 35m, and not 10, 20, 30 or 17m?

## Slide 6: cLHS using ArcGIS and R
The soil mapping project anticipates use of digital soil mapping techniques with 5m resolution data
Data values from the samples must match the values of the covariate layers, since the sample points will serve as training data for modelling work
Using resample or aggregate to a random output resolution would alter output data values with no correspondence between training point and the 5m cell values

## Slide 7: cLHS using ArcGIS and R
Resampling to resolutions that are odd, e.g. 3x,5x,7x,9x… will insure co-registration with input cells provided:
The processing extent and snap raster are set to
one of the 5m layers using the ArcGIS “Environment
Settings”
Resample one of the 5m rasters to 35m, e.g. slope gradient
Use “Bilinear”
or “Cubic”resampling

## Slide 8: cLHS using ArcGIS and R
Convert the 35m raster to a point file
Verify the 35m points are centered in the 5m cells

## Slide 9: cLHS using ArcGIS and R
Run Extract Multi Values to Points to associate cell
values from the 5m slope gradient, slope curvature and
wetness index layers to points

## Slide 10: cLHS using ArcGIS and R
Sample of the attribute table of point file
An example shapefile named “points_35m.*”, that is the result of all previous steps is available for your use
Slope gradient, curvature, wetness index

## Slide 11: cLHS using ArcGIS and R
Open the attribute table of point file in ArcGIS
Sort by POINTID
Hide all data fields except slope gradient, slope curvature, and wetness index

## Slide 12: cLHS using ArcGIS and R
Export as a text file, e.g. “input_clhs.txt”
This will be the input file for the cLHS package in R
and has been supplied as a starting point for this
example

## Slide 13: cLHS using ArcGIS and R
Download and run sample R script

## Slide 14: cLHS using ArcGIS and R
Open the output file in a text editor and edit the column header of the first field to be sure it is named “id” or “ID”
This insures that the output file from cLHS can be joined to the original point file in ArcGIS using the POINTID and ID respectively as join fields

## Slide 15: cLHS using ArcGIS and R
Run “Add XY Coordinates” in ArcGIS on the original point file
Join the original point file to the cLHS output text file
Run “Make XY Event Layer” in ArcGIS on the table from step #2
Convert the Layer from step #3 to a feature
Use the file from step #4 as input waypoints for use with a GPS receiver to navigate to samples